## Slide 1
UAV Planning, Autonomous Tracking, and Obstacle Identification and Avoidance
Álvaro Melgosa Pascual
Notes: UAV=Unmanned Aerial Vehicle

## Slide 2
Outline
SAFETY
Motivation

## Slide 3
Problem statement
Is it possible to improve the operational safety of a wide range of UAVs by developing an intermediate functional layer that prevents physical collisions between the UAV and its surroundings?
Motivation
Notes: Repeat explanation of concepts from the Thesis

## Slide 4
Methodology
Systems Engineering collects and organises all the information needed to understand the whole problem, explores it from all angles, and then finds the most appropriate system solution.
Richard Beasley, Rolls-Royce Global Chief of Systems Engineering, 2015
Motivation
Notes: Systems Engineering provides a set of tools that facilitate the systematic analysis of the needs of any system

## Slide 5
Objectives
Design an OCAS
Integrate it within existing UAVs
Build and test a working prototype
Demonstrate that safety is improved
Motivation

## Slide 6
Result
A system that is:
Reliable
Modular
Expandable
Open
Motivation
Notes: Result: a system that is reliable, modular, expandable and open
Open is a important property since it allows future research and improvements
It constitutes a base on which technology can be further developed and fitted to any specific need

## Slide 7
Outline
SAFETY
Motivation
Design
What?

## Slide 8
Design
Requirements
A statement or characteristic of something that is needed.
Notes: A requirement is a statement or characteristic of something that is needed.
For the case of the OCAS, they represent the set of features and objectives that the system must accomplish to meet the final goal of the OCAS: Avoid collisions against Obstacles
The requirements document is accessible to the whole design team and should be constantly updated (live or evolving document)
In Systems Engineering requirements drive design

## Slide 9
Design
Requirements
The OCAS shall:
Improve the operational safety of the UAV
Avoid collisions against obstacles
Work independently of the UAV
Not interfere with existing UAV functions
Be operable after a short training by any pilot
Notes: Example of most significant requirements.
“Avoid collisions” can be thought as derived from the “Improve operational safety” requirement
Work independently -> To enhance modularity and upgradeability
Not interfere -> Change behaviour of the UAV only when there is risk of collision

## Slide 10
Design
Logical decomposition
Decomposes the requirements
Helps build a system architecture
Notes: Decomposes the requirements and helps build a system architecture by identifying the functions that must be performed
Also called Functional analysis

## Slide 11
Design
Functional Flow Block Diagram
Notes: FFBD represents the sequential order of execution of the defined functions to complete a successful mission
Inside dashed red line are the functions performed by the OCAS (scope)
This is the top level of functions, each one is composed by several subfunctions

## Slide 12
Design
Functional Flow Block Diagram

## Slide 13
Design
Functional Flow Block Diagram

## Slide 14
Design
Product Breakdown Structure
Notes: PBS represents the system physical architecture, derived from the functional architecture
Most important elements for the OCAS are the Computer board and the Software

## Slide 15
Design
N2 diagram
Notes: Most important elements from the PBS in the diagonal
Outputs from each of the elements in their horizontal rows
Inputs to each element in the vertical columns
Green paths: UAS without OCAS
Yellow paths: Classic control problem
Blue path: Logging information
Black paths: Pysical interfaces
EXAMPLE: Start in processing unit -> end in avoidance manoeuvre by UAV

## Slide 16
Outline
SAFETY
Motivation
Implementation
Design
What?
How?

## Slide 17
Implementation
Integration with the UAS
Notes: UAS = Unmanned Aerial System. Contains (one or more) UAVs, GCS and any other element relevant for the operation of the UAV

## Slide 18
Implementation
Integration with the UAS
Notes: OCAS will be embarked on the UAV, holding a second wireless connection with the GCS

## Slide 19
Implementation
Component choice
Sensors
Alternatives:
Radar
Sonar
Lidar
Computer vision
Evaluation criteria:
Range
Accuracy
Flexibility
Weight
Cost
Ease of operation
Ease of integration
Notes: Trade-off study between all the possible alternatives, evaluating each of them on all of the criteria
More detail in the paper

## Slide 20
Implementation
Component choice
Sonar HC-SR04
Notes: Advantages: Light weight, low cost, simple operation (trigger-echo), easy processing (multiply time by speed of sound -> distance to closest object)
Disadvantages: Noisy environments, ghost signals and multipath errors

## Slide 21
Implementation
Component choice
Raspberry Pi
Full computer
Credit card size
Linux OS
GPIO pins
4x USB ports
Networking capable
Notes: Alternative: Microcontroller board (Arduino). Less computationally capable, no Operating System, no networking… -> more limited

## Slide 22
Implementation
OCAS interfaces
Notes: Everything considered part of the OCAS is enclosed in the blue box
The Raspberry Pi is the main controller, where all the other elements are connected
SSH: allows for the remote access to the Linux terminal from the GCS
MAVlink: is the comunication protocol for all Ardupilot UAVs. Both low and high level commands (examples)
GPIO: Regular wires. State of the pins can be set LOW or HIGH (that is, 0V or 3.3V) via software

## Slide 23
Implementation
Software interfaces
Notes: Schematic derived from the N2 diagram
Inside the Raspberry Pi, Raspbian OS provides some utilities that allow for easy connection of the external components
Also, it can run a Python environment, under which all the other functions have been developed
First, from the SSH interface, the operator has access to the Linux Shell, from which the Graphical User Interface can be launched
From the GUI, MAVproxy and the Control script can be launched with the appropriate parameters
MAVproxy connects to the vehicle via one of the USB ports and pipes the MAVlink messages to the Control script
The script takes that information, together with the one retrieved from the sonar, and processes it in the way that was shown in the FFBD (more information later)
Finally, if an actuation is required, a MAVlink message is sent back to the UAV through the MAVproxy software

## Slide 24
Implementation
The Python script
Notes: According to the PBS, any component of the system that has not been covered yet needs to be implemented in the Python script
Flowchart of functions, following the FFBD. EXPLAIN
Dashed lines represent information flow, not sequential order

## Slide 25
Implementation
The Python script
Notes: Consider these specific functions for a deeper analysis

## Slide 26
Implementation
Evaluate level of threat
Notes: Assuming any instant of time when the distance to the detected obstace is x0 and the velocity is v0, a linear extrapolation can be done to predict the time remaining to the collision.
Now, considering the reaction time of the script to take control of the vehicle, the estimated time to stop the UAV at the current speed and some margin for errors, I claim that the scenario is unsafe when tsafe, defined as shown below, is smaller than 0.
That is, the UAV has less time to stop and prevent the collision than the available time to the collision itself.
Hence, the avoidance manouvre will be triggered when tsafe<0

## Slide 27
Implementation
Avoid obstacle
In the future:
Real time control
Fused data from sonars + onboard sensors
At the moment:
Guided mode (loiter)
“Go to” functions based on GPS data
Notes: This stage only developed as a proof of concept. Functional enough to avoid a collision
Great chance of improvement, with sophisticated signal processing techniques
Concepts of navigation and trajectory planning could be incorporated

## Slide 28
Outline
SAFETY
Motivation
Testing
Implementation
Design
What?
How?
Does it work?

## Slide 29
Testing
Testing platform
Notes: The testing platform consists on a Ready To Fly F450 frame with some modifications to allocate the additional components

## Slide 30
Testing
Testing setup
Open space
Great GPS coverage
“Safe” obstacle
Compliant with local regulations

## Slide 31
Testing
Flight procedure
Connect OCAS to GCS
Connect OCAS to UAV
Start Python script
Take off
Approach obstacle frontally
Fingers crossed
Regain control of UAV
Land
Notes: According to FFBD

## Slide 32
Testing
Flight test

## Slide 33
Testing
Flight test
Notes: This information is taken from 3 different log files
From the Ardupilot log, the altitude and position
From the GCS log, the flight modes
From the script log, the sensor events

## Slide 34
Outline
SAFETY
Motivation
Testing
Implementation
Design
What?
How?
Is the goal met?
Does it work?

## Slide 35
Conclusion

## Slide 36
THANK YOU

## Slide 37
Conclusion
Conclusions
Big potential for safety improvements
Other sensing options might be interesting
Systematic design procedures are critical for complex systems
The definition of interfaces is critical for the communication with the external systems
Systematically testing and validating the design and implementation is crucial
Notes: There exists a large capacity of improvement in terms of the safety levels that could be achieved during the operation of UAVs
The ultrasonic rangefinders have been chosen mainly for their ease of use and small processing requirements. Other options might lead to better results
Variables and assumptions are difficult to track during the design phase if Systems Engineering approach hadn’t been taken
The definition of the interfaces is of utmost importance for the system to work as a whole and properly perform its functions
Testing prevents more serious errors down the road, which would be more difficult to correct

## Slide 38
Conclusion
Contributions
Designed a safety layer that can improve the safety of numerous UAVs during operation, to improve their situational awareness
Implemented the proposed conceptual design as a proof of concept
Built a working prototype to show that the solution is functional and answers positively to the problem statement
Notes: The OCAS allows for a higher level of safety, allowing the pilot to better perform the misión
With the implementation of the concept, the basic building blocks are perfectly defined, and future work can focus on improving each of the components separately
The working prototype confirms that the proposed design is suitable to solve the problem, and proves that the objectives have been met

## Slide 39
Conclusion
Future work
Improve the acquisition of data from the sensors
Try different sensors, or fuse the data
Better prediction of the trajectory
Implement real-time control algorithms
Apply the OCAS to real life problems
Notes: Data acquisition has great potential to improve: Triggering procedures, noise filtering, signal processing…
Sonars are just an alternative from all the sensors that could be used. Other types of sensors can provide additional information. Sensor fusion is a good way of obtaining new information from existing data
Better calculation of the trajectory would allow for a better prediction of the potential collisions
Real-time control algoritms would avoid the complete reliance on a quality GPS signal of the present impementation
Find a real application for the Obstacle Collision Avoidance System

## Slide 40
Potential UAV markets in 2015
Source: PwC Global

## Slide 41
Sensor trade-off study

## Slide 42
Implementation
Evaluate distance
Notes: With a 10us signal on the trigger pin of the sonar, it automatically sends a sequence of ultrasonic signals
It recieves those signals if rebounded against an obstacle and calculates the time of arrival
An ouput signal of the same lenght in time is returned through the echo pin
Notice the dependency of the measured distance on the environmental temperature.
However, a temperature difference of 10ºC w.r.t the reference induces errors of the order of 1mm, so negligible

## Slide 43
Implementation
Compute velocity
First order backward differences with a three-data-point stencil
Notes: Why? Because the signal is noisy, and differentiating a noisy signal amplifyes the noise (the differentiation is a perfect high-pass filter)
This approach has better damping properties than conventional differentiation, so that better predictions of position can be made

## Slide 44
Implementation
Compute velocity
First order backward differences with a three-data-point stencil
Notes: EXAMPLE
Imagine that the last measurement (t0) is not correct for some reason

## Slide 45
Implementation
Compute velocity
First order backward differences with a three-data-point stencil
Notes: Computing the slope of the last interval and propagating into the future yields to an even bigger error

## Slide 46
Implementation
Compute velocity
First order backward differences with a three-data-point stencil
Notes: Instead, with the two-data-point stencil, the error is dampened, while maintaining relatively responsive predicting capabilities on the future location of the obstacle

## Slide 47
Implementation
The Python environment
GUI
MAVproxy
Control script
Notes: GUI: Select connection method, and connection fields autocomplete with the default settings.
Connect button launches MAVproxy with the specified settings and pipes the information to the script
GUI: Write the name of the folder where the main.py file of the script is located, and run it
The script is composed of several Python files, which I’ll try to give an overview of.

## Slide 48
Sonar limitations

## Slide 49
Main.py

## Slide 50
Main.py

## Slide 51
Main.py

## Slide 52
Sonar.py

## Slide 53
Control.py

## Slide 54
Auto.py

## Slide 55
Temperature sensitivity