## Slide 1
UAV Planning, Autonomous Tracking, and Obstacle Identification and Avoidance
Álvaro Melgosa Pascual
Notes: UAV=Unmanned Aerial Vehicle

## Slide 2
Motivation
Notes: First of all, what do I want to achieve?
What is the purpose of this Thesis?

## Slide 3
Safety
Motivation
Notes: Most important issue in aerospace industry
UAVs can be considered part of aerospace industry, but not so safe
Disembarking the human eliminates intuitive sensing (inertial, visual, noise…)
Sensing has to be done by sensors and interpreted by computers for safe autonomous flight

## Slide 4
Safety
Improved
OCAS
Motivation
Notes: OCAS (similarly to TCAS in commercial aircraft) tries to eliminate the posibility of a physical collision of the UAV with its surroundings
OCAS operates as intermediate functional layer between operator and UAV

## Slide 5
Example: DJI Phantom 4
Source: dji.com
Motivation
Notes: Why is it important to have a reliable Obstacle Collision Avoidance System?
DJI recently (March 2016) built one into their Phantom 4
Based on stereoscopic cameras

## Slide 6
Regular operation
Source: gizmodo.com
Motivation
Notes: Gizmodo journalists were testing the new features of the UAV
In particular the Emergency mode, that stops the vehicle when a collision is about to happen

## Slide 7
Faulty operation
Source: gizmodo.com
Motivation
Notes: However, there are sometimes (Sport mode) that the Emergency mode is deactivated
The journalist was relying on that safety system while testing other features, and accidentally crashed the UAV

## Slide 8
Problem statement
Is it possible to improve the operational safety of a wide range of UAVs by developing an intermediate functional layer that prevents physical collisions between the UAV and its surroundings?
Motivation
Notes: Repeat explanation of concepts from the Thesis

## Slide 9
Objectives
Design an OCAS
Integrate it within existing UAVs
Build a working prototype
Demonstrate that safety is improved
Motivation

## Slide 10
Methodology
Systems Engineering collects and organises all the information needed to understand the whole problem, explores it from all angles, and then finds the most appropriate system solution.
Richard Beasley, Rolls-Royce Global Chief of Systems Engineering, 2015
Motivation
Notes: Systems Engineering provides a set of tools that facilitate the systematic analysis of the needs of any system

## Slide 11
Result
A system that is:
Reliable
Modular
Expandable
Open
Motivation
Notes: Result: a system that is reliable, modular, expandable and open
Open is a important property since it allows future research and improvements
It constitutes a base on which technology can be further developed and fitted to any specific need

## Slide 12
Outline
SAFETY
Motivation
Testing
Implementation
Design
Requirements
Logical decomposition
Results
Prototype

## Slide 13
1.
Outline
2.
3.
Design
Implementation
Testing

## Slide 14
Design
Notes: Conceptual design of the OCAS
Accomplishes its functions, but is not limited to specific components
The conceptual design can be fitted to different needs during the implementation phase

## Slide 15
Design
The design process
Notes: The design process in Systems Engineering is iterative, and the product is improved in each iteration.
In the Requirements loop, it is defined what the system must do (requirements) and the elements needed to perform all those functions (logical decomposition)
In the Design loop, the system is designed and built according to the architectures defined in the Logical decomposition step, identifying issues and propagating back if needed

## Slide 16
Design
Requirements
A statement or characteristic of something that is needed.
Notes: A requirement is a statement or characteristic of something that is needed.
For the case of the OCAS, they represent the set of features and objectives that the system must accomplish to meet the final goal of the OCAS: Avoid collisions against Obstacles
The requirements document is accessible to the whole design team and should be constantly updated (live or evolving document)
In Systems Engineering requirements drive design

## Slide 17
Design
Requirements
Come from:
Customer needs → Motivation
Regulations
Defined goals and objectives
Assumptions and constraints
Notes: The requirements (what the system must do) can come from:
Motivation instead of customer needs because there is no customer

## Slide 18
Design
Requirements
The OCAS shall:
Improve the operational safety of the UAV
Avoid collisions with the detected obstacles
Work independently of the UAV
Not interfere with existing UAV functions
Be operable after a short training by any pilot
Notes: Example of most significant requirements.
“Avoid collisions” can be thought as derived from the “Improve operational safety” requirement
Work independently -> To enhance modularity and upgradeability
Not interfere -> Change behaviour of the UAV only when there is risk of collision

## Slide 19
Design
Logical decomposition
Decomposes the requirements
Helps build a system architecture
Notes: Decomposes the requirements and helps build a system architecture by identifying the functions that must be performed
Also called Functional analysis

## Slide 20
Design
Logical decomposition
Tools
Functional architecture
N2 diagram
PBS
FFBD
Notes: There are many tools for the logical decomposition of the system
Functional architecture: Hierarchical representation of all the functions
FFBD: Sequential order of the functions during a mission
PBS: Set of elements that need to be included in the system to perform all the identified functions
N2: Interfaces between the elements identified in the PBS

## Slide 21
Design
Functional Flow Block Diagram
Notes: FFBD represents the sequential order of execution of the defined functions to complete a successful mission
Inside dashed red line are the functions performed by the OCAS (scope)
This is the top level of functions, each one is composed by several subfunctions

## Slide 22
Design
Functional Flow Block Diagram
Notes: Most critical functions are “detect” and “avoid”
Monitor environment function is working in an endless loop
When the situation is considered as unsafe, the avoid function gets triggered
Skip over functional architecture

## Slide 23
Design
Product Breakdown Structure
Notes: PBS represents the system physical architecture, derived from the functional architecture
Most important elements for the OCAS are the Computer board and the Software

## Slide 24
Design
N2 diagram
Notes: Most important elements from the PBS in the diagonal
Outputs from each of the elements in their horizontal rows
Inputs to each element in the vertical columns
Green paths: UAS without OCAS
Yellow paths: Classic control problem
Blue path: Logging information
Black paths: Pysical interfaces
EXAMPLE: Start in processing unit -> end in avoidance manoeuvre by UAV

## Slide 25
Implementation
Notes: After the Requirements, Funcional architecture, FFBD, PBS and N2 diagram, we have a comprehensive idea of WHAT the system must do and the tools and elements that will help it do it, together with the communications that need to be established.
Now it is time to implement all these concepts from the conceptual design into an actual product, which is able to meet the specifications

## Slide 26
Implementation
Integration with the UAS
Notes: UAS = Unmanned Aerial System. Contains (one or more) UAVs, GCS and any other element relevant for the operation of the UAV

## Slide 27
Implementation
Integration with the UAS
Notes: OCAS will be embarked on the UAV, holding a second wireless connection with the GCS

## Slide 28
Implementation
Component choice
Sensors
Alternatives:
Radar
Sonar
Lidar
Computer vision
Evaluation criteria:
Range
Accuracy
Flexibility
Weight
Cost
Ease of operation
Ease of integration
Notes: Trade-off study between all the possible alternatives, evaluating each of them on all of the criteria
More detail in the paper

## Slide 29
Implementation
Component choice
Sonar HC-SR04
Notes: Advantages: Light weight, low cost, simple operation (trigger-echo), easy processing (multiply time by speed of sound -> distance to closest object)
Disadvantages: Noisy environments, ghost signals and multipath errors

## Slide 30
Implementation
Component choice
Raspberry Pi
Full computer
Credit card size
Linux OS
GPIO pins
4x USB ports
Networking capable
Notes: Alternative: Microcontroller board (Arduino). Less computationally capable, no Operating System, no networking… -> more limited

## Slide 31
Implementation
Other components
Power source
WiFi adapter
Testing platform
Notes: Battery according to the requierement of independency with the UAV. Provides 2.4 A to the Raspberry Pi
WiFi adapter for the wireless communication with the GCS, as shown before
Testing platform based on Maite Arteta’s Thesis from 2015

## Slide 32
Implementation
OCAS interfaces
Notes: Everything considered part of the OCAS is enclosed in the blue box
The Raspberry Pi is the main controller, where all the other elements are connected
SSH: allows for the remote access to the Linux terminal from the GCS
MAVlink: is the comunication protocol for all Ardupilot UAVs. Both low and high level commands (examples)
GPIO: Regular wires. State of the pins can be set LOW or HIGH (that is, 0V or 3.3V) via software

## Slide 33
Implementation
Software interfaces
Notes: Schematic derived from the N2 diagram
Inside the Raspberry Pi, Raspbian OS provides some utilities that allow for easy connection of the external components
Also, it can run a Python environment, under which all the other functions have been developed
First, from the SSH interface, the operator has access to the Linux Shell, from which the Graphical User Interface can be launched
From the GUI, MAVproxy and the Control script can be launched with the appropriate parameters
MAVproxy connects to the vehicle via one of the USB ports and pipes the MAVlink messages to the Control script
The script takes that information, together with the one retrieved from the sonar, and processes it in the way that was shown in the FFBD (more information later)
Finally, if an actuation is required, a MAVlink message is sent back to the UAV through the MAVproxy software

## Slide 34
Implementation
The Python environment
GUI
MAVproxy
Control script
Notes: GUI: Select connection method, and connection fields autocomplete with the default settings.
Connect button launches MAVproxy with the specified settings and pipes the information to the script
GUI: Write the name of the folder where the main.py file of the script is located, and run it
The script is composed of several Python files, which I’ll try to give an overview of.

## Slide 35
Implementation
The Python script
Notes: According to the PBS, any component of the system that has not been covered yet needs to be implemented in the Python script
Flowchart of functions, following the FFBD. EXPLAIN
Dashed lines represent information flow, not sequential order

## Slide 36
Implementation
The Python script
Notes: Consider these specific functions for a deeper analysis

## Slide 37
Implementation
Evaluate distance
Notes: With a 10us signal on the trigger pin of the sonar, it automatically sends a sequence of ultrasonic signals
It recieves those signals if rebounded against an obstacle and calculates the time of arrival
An ouput signal of the same lenght in time is returned through the echo pin
Notice the dependency of the measured distance on the environmental temperature.
However, a temperature difference of 10ºC w.r.t the reference induces errors of the order of 1mm, so negligible

## Slide 38
Implementation
Compute velocity
First order backward differences with a three-data-point stencil
Notes: Why? Because the signal is noisy, and differentiating a noisy signal amplifyes the noise (the differentiation is a perfect high-pass filter)
This approach has better damping properties than conventional differentiation, so that better predictions of position can be made

## Slide 39
Implementation
Compute velocity
First order backward differences with a three-data-point stencil
Notes: EXAMPLE
Imagine that the last measurement (t0) is not correct for some reason

## Slide 40
Implementation
Compute velocity
First order backward differences with a three-data-point stencil
Notes: Computing the slope of the last interval and propagating into the future yields to an even bigger error

## Slide 41
Implementation
Compute velocity
First order backward differences with a three-data-point stencil
Notes: Instead, with the two-data-point stencil, the error is dampened, while maintaining relatively responsive predicting capabilities on the future location of the obstacle

## Slide 42
Implementation
Evaluate level of threat
Notes: Assuming any instant of time when the distance to the detected obstace is x0 and the velocity is v0, a linear extrapolation can be done to predict the time remaining to the collision.
Now, considering the reaction time of the script to take control of the vehicle, the estimated time to stop the UAV at the current speed and some margin for errors, I claim that the scenario is unsafe when tsafe, defined as shown below, is smaller than 0.
That is, the UAV has less time to stop and prevent the collision than the available time to the collision itself.
Hence, the avoidance manouvre will be triggered when tsafe<0

## Slide 43
Implementation
Avoid obstacle
In the future:
Real time control
Fused data from sonars + onboard sensors
At the moment:
Guided mode (loiter)
“Go to” functions based on GPS data
Notes: This stage only developed as a proof of concept. Functional enough to avoid a collision
Great chance of improvement, with sophisticated signal processing techniques
Concepts of navigation and trajectory planning could be incorporated

## Slide 44
Testing
Notes: The testing phase is critical to ensure that the designed system meets the specifications
Of course, all the components and subsystems should be tested thoroughly, but for the 1st prototype it was only done for the most critical components: sensors, connections, software, and the final prototype
The test were mostly performed in parallel to the implementation phase, influencing in some of the decisions taken
Now, for the sake of time, only the complete OCAS tests will be covered here. The rest can be found in the Thesis

## Slide 45
Testing
Testing platform
Notes: The testing platform consists on a Ready To Fly F450 frame with some modifications to allocate the additional components

## Slide 46
Testing
Testing setup
Open space
Great GPS coverage
“Safe” obstacle
Compliant with local regulations

## Slide 47
Testing
Flight procedure
Connect OCAS to GCS
Connect OCAS to UAV
Start Python script
Take off
Approach obstacle frontally
Fingers crossed
Regain control of UAV
Land
Notes: According to FFBD

## Slide 48
Testing
Flight test

## Slide 49
Testing
Flight test
Notes: This information is taken from 3 different log files
From the Ardupilot log, the altitude and position
From the GCS log, the flight modes
From the script log, the sensor events

## Slide 50
Conclusion
Notes: Goal of the Project was to make Unmanned flight safer by providing a modular Obstacle Collision Avoidance System

## Slide 51
THANK YOU
Notes: Consider finishing here

## Slide 52
Conclusion
Conclusions
Big potential for safety improvements
Other sensing options might be interesting
Systematic design procedures are critical for complex systems
The definition of interfaces is critical for the communication with the external systems
Systematically testing and validating the design and implementation is crucial
Notes: There exists a large capacity of improvement in terms of the safety levels that could be achieved during the operation of UAVs
The ultrasonic rangefinders have been chosen mainly for their ease of use and small processing requirements. Other options might lead to better results
Variables and assumptions are difficult to track during the design phase if Systems Engineering approach hadn’t been taken
The definition of the interfaces is of utmost importance for the system to work as a whole and properly perform its functions
Testing prevents more serious errors down the road, which would be more difficult to correct

## Slide 53
Conclusion
Contributions
Designed a safety layer that can improve the safety of numerous UAVs during operation, to improve their situational awareness
Implemented the proposed conceptual design as a proof of concept
Built a working prototype to show that the solution is functional and answers positively to the problem statement
Notes: The OCAS allows for a higher level of safety, allowing the pilot to better perform the misión
With the implementation of the concept, the basic building blocks are perfectly defined, and future work can focus on improving each of the components separately
The working prototype confirms that the proposed design is suitable to solve the problem, and proves that the objectives have been met

## Slide 54
Conclusion
Future work
Improve the acquisition of data from the sensors
Try different sensors, or fuse the data
Better prediction of the trajectory
Implement real-time control algorithms
Apply the OCAS to real life problems
Notes: Data acquisition has great potential to improve: Triggering procedures, noise filtering, signal processing…
Sonars are just an alternative from all the sensors that could be used. Other types of sensors can provide additional information. Sensor fusion is a good way of obtaining new information from existing data
Better calculation of the trajectory would allow for a better prediction of the potential collisions
Real-time control algoritms would avoid the complete reliance on a quality GPS signal of the present impementation
Find a real application for the Obstacle Collision Avoidance System

## Slide 55
THANK YOU

## Slide 56
Potential UAV markets in 2015
Source: PwC Global

## Slide 57
Sensor trade-off study

## Slide 58
Sonar connection

## Slide 59
MAVlink flow diagram

## Slide 60
Sonar limitations

## Slide 61
Main.py

## Slide 62
Main.py

## Slide 63
Main.py

## Slide 64
Sonar.py

## Slide 65
Control.py

## Slide 66
Auto.py

## Slide 67
Temperature sensitivity