## Slide 1
UAV Planning, Autonomous Tracking, and Obstacle Identification and Avoidance
Álvaro Melgosa Pascual
1
Notes: UAV=Unmanned Aerial Vehicle

## Slide 2
Motivation
Notes: First of all, why am I doing this?
What is the purpose of this Thesis?

## Slide 3
Safety
Motivation
Notes: Most important issue in aerospace industry
UAVs can be considered part of aerospace industry, but not so safe
Disembarking the human eliminates intuitive sensing (inertial, visual, noise…)
Sensing has to be done by sensors and interpreted by computers for safe autonomous flight

## Slide 4
Safety
Improved
OCAS
Motivation
Notes: OCAS (similarly to TCAS in commercial aircraft) tries to eliminate the posibility of a physical collision of the UAV with its surroundings
OCAS operates as intermediate functional layer between operator and UAV

## Slide 5
Example: DJI Phantom 4
Source: dji.com
Motivation
Notes: Why is it important to have a reliable Obstacle Collision Avoidance System?
DJI recently (March 2016) built one into their Phantom 4
Based on stereoscopic cameras

## Slide 6
Regular operation
Source: gizmodo.com
Motivation
Notes: Gizmodo journalists were testing the new features of the UAV
In particular the Emergency mode, that stops the vehicle when a collision is about to happen

## Slide 7
Faulty operation
Source: gizmodo.com
Motivation
Notes: However, there are sometimes (Sport mode) that the Emergency mode is deactivated
The journalist was relying on that safety system while testing other features, and accidentally crashed the UAV

## Slide 8
Problem statement
Is it possible to improve the operational safety of a wide range of UAVs by developing an intermediate functional layer that prevents physical collisions between the UAV and its surroundings?
Motivation
Notes: Explanation from the Thesis

## Slide 9
Objectives
Design an OCAS
Integrate is within existing UAVs
Build a working prototype
Demonstrate that safety is improved
Motivation

## Slide 10
Methodology
Systems Engineering collects and organises all the information needed to understand the whole problem, explores it from all angles, and then finds the most appropriate system solution.
Richard Beasley, president of INCOSE UK, 2015
Motivation
Notes: Systems Engineering provides a set of tools that facilitate the systematic analysis of the needs of any system
INCOSE = INternational COuncil of Systems Engineering

## Slide 11
Result
A system that is:
Reliable
Modular
Expandable
Open
Motivation
Notes: Result: a system that is reliable, modular, expandable and open
Open is a important property since it allows future research and improvements
It constitutes a base on which technology can be further developed and fitted to any specific need

## Slide 12
1.
Outline
2.
3.
Design
Implementation
Testing

## Slide 13
Design
The design process
Notes: The design process in Systems Engineering is iterative, and the product is improved in each iteration.
In the Requirements loop, it is defined what the system must do (requirements) and the elements needed to perform all those functions (logical decomposition)
In the Design loop, the system is designed and built according to the architectures defined in the Logical decomposition step, identifying issues and propagating back if needed

## Slide 14
Design
Requirements
A statement or characteristic of something that is needed.
Notes: A requirement is a statement or characteristic of something that is needed.
For the case of the OCAS, they represent the set of features and objectives that the system must accomplish to meet the final goal of the OCAS: Avoid collisions against Obstacles
The requirements document is accessible to the whole design team and should be constantly updated (live or evolving document)
In Systems Engineering requirements drive design

## Slide 15
Design
Requirements
Come from:
Customer needs → Motivation
Regulations
Defined goals and objectives
Assumptions and constraints
Notes: The requirements (what the system must do) can come from:
Motivation instead of customer needs because there is no customer

## Slide 16
Design
Requirements
The OCAS shall:
Improve the operational safety of the UAV
Avoid collisions with the detected obstacles
Work independently of the UAV
Not interfere with existing UAV functions
Be accessible from the GCS
Be operable after a short training by any pilot
Notes: Example of most significant requirements.
“Avoid collisions” can be thought as derived from the “Improve operational safety” requirement
Work independently -> To enhance modularity and upgradeability
Not interfere -> Change behaviour of the UAV only when there is risk of collision
GCS = Ground Control Station

## Slide 17
Design
Logical decomposition
Decomposes the requirements
Helps build a system architecture
Notes: Decomposes the requirements and helps build a system architecture by identifying the functions that must be performed
Also called Functional analysis

## Slide 18
Design
Logical decomposition
Tools
Functional architecture
N2 diagram
PBS
FFBD
Notes: There are many tools for the logical decomposition of the system
Functional architecture: Hierarchical representation of all the functions
FFBD: Sequential order of the functions during a mission
PBS: Set of elements that need to be included in the system to perform all the identified functions
N2: Interfaces between the elements identified in the PBS

## Slide 19
Design
Functional Flow Block Diagram
Notes: FFBD represents the sequential order of execution of the defined functions to complete a successful misión
Inside dashed red line are the functions performed by the OCAS (scope)
This is the top level of functions, each one is composed by several subfunctions

## Slide 20
Design
Functional Flow Block Diagram
Notes: Most critical functions are “detect” and “avoid”
Monitor environment function is working in an endless loop
When the situation is considered as unsafe, the avoid function gets triggered
Skip over functional architecture

## Slide 21
Design
Product Breakdown Structure
Notes: PBS represents the system physical architecture, derived from the functional architecture
Most important elements for the OCAS are the Computer board and the Software

## Slide 22
Design
N2 diagram
Notes: Most important elements from the PBS in the diagonal
Outputs from each of the elements in their horizontal rows
Inputs to each element in the vertical columns
Green paths: UAS without OCAS
Yellow paths: Classic control problema
Blue path: Logging information
Black paths: Pysical interfaces
EXAMPLE: Start in processing unit -> end in avoidance manoeuvre by UAV

## Slide 23
Implementation
Notes: After the Requirements, Funcional architecture, FFBD, PBS and N2 diagram, we have a comprehensive idea of WHAT the system must do and HOW it must do it, together with the communications that need to be established.
Now it is time to implement all these concepts from the conceptual design into an actual product, which is able to meet the specifications

## Slide 24
Implementation
Integration with the UAS
Notes: UAS = Unmanned Aerial System. Contains (one or more) UAVs, GCS and any other element relevant for the operation of the UAV

## Slide 25
Implementation
Integration with the UAS
Notes: OCAS will be embarked on the UAV, holding a second wireless connection with the GCS

## Slide 26
Implementation
Component choice
Sensors
Alternatives:
Radar
Sonar
Lidar
Computer vision
Evaluation criteria:
Range
Accuracy
Flexibility
Weight
Cost
Ease of operation
Ease of integration
Notes: Trade-off study between all the possible alternatives, evaluating each of them on all of the criteria
More detail in the paper

## Slide 27
Implementation
Component choice
Sonar HC-SR04
Notes: Advantages: Light weight, low cost, simple operation (trigger-echo), easy processing (multiply time by speed of sound -> distance to closest object)
Disadvantages: Noisy environments, ghost signals and multipath errors

## Slide 28
Implementation
Component choice
Raspberry Pi
Full computer
Credit card size
Linux OS
GPIO pins
4x USB ports
Networking capable
Notes: Alternative: Microcontroller board (Arduino). Less computationally capable, no Operating System, no networking… -> more limited

## Slide 29
Implementation
Other components
Power source
WiFi adapter
Testing platform
Notes: Battery according to the requierement of independency with the UAV. Provides 2.4 A to the Raspberry Pi
WiFi adapter for the wireless communication with the GCS, as shown before
Testing platform based on Maite Arteta’s Thesis from 2015

## Slide 30
Implementation
OCAS interfaces
Notes: Everything considered part of the OCAS is enclosed in the blue box
The Raspberry Pi is the main controller, where all the other elements are connected
SSH: allows for the remote access to the Linux terminal from the GCS
MAVlink: is the comunication protocol for all Ardupilot UAVs. Both low and high level commands (examples)
GPIO: Regular wires. State of the pins can be set LOW or HIGH (that is, 0V or 3.3V) via software

## Slide 31
Implementation
Software interfaces
Notes: Schematic derived from the N2 diagram
Inside the Raspberry Pi, Raspbian OS provides some utilities that allow for easy connection of the external components
Also, it can run a Python environment, under which all the other functions have been developed
First, from the SSH interface, the operator has access to the Linux Shell, from which the Graphical User Interface can be launched
From the GUI, MAVproxy and the Control script can be launched with the appropriate parameters
MAVproxy connects to the vehicle via one of the USB ports and pipes the MAVlink messages to the Control script
The script takes that information, together with the one retrieved from the sonar, and processes it in the way that was shown in the FFBD (more information later)
Finally, if an actuation is required, a MAVlink message is sent back to the UAV through the MAVproxy software

## Slide 32
Implementation
The Python environment
GUI
MAVproxy
Control script
Notes: GUI: Select connection method, and connection fields autocomplete with the default settings.
Connect button launches MAVproxy with the specified settings and pipes the information to the script
GUI: Write the name of the folder where the main.py file of the script is located, and run it
The script is composed of several Python files, which I’ll try to give an overview of.

## Slide 33
Implementation
The Python script

## Slide 34
Implementation

## Slide 35
Testing

## Slide 36
Testing

## Slide 37
Testing

## Slide 38
Conclusions

## Slide 39
Conclusions

## Slide 40
Conclusions